## Slide 1: Connected Corridors I-210 Corridor Analysis, Modeling & Simulation
July 16, 2014
Date: August 13, 2014
Caltrans District 7

## Slide 2: Introduction to AMS on the I-210 Corridor
Why AMS
  Enhance common understanding among stakeholders
  Test the applicability of various control strategies based on ramp meters, signal lights, and the managed routing of travelers (roads, transit, etc.)
  Provide justification for repairing and upgrading both sensing infrastructure and control elements
Outputs
  AMS Final Report: Evaluation of ICM benefits and costs
  Generation of strategies and response plans for use in the Concept of Operations
  Better understanding of System Engineering Requirements

## Slide 3: AMS on the I-210 Corridor
Assess Operations
Select Interventions
Evaluate
Simulate
Create Models
Select Scenarios
Assess Costs

## Slide 4: Outline for AMS Final Report
Introduction and background
Corridor description
AMS methodology
  Modelling approach
  Simulation model
  Data requirements
Analysis scenarios and ICM strategies
Model calibration approach and methodology
  Calibration acceptance criteria
  Validation
Performance measures
  Mobility and other metrics
  Framework for costs/benefits analysis
ICM deployment analysis findings
  Overall ICM performance
  ICM benefits
  ICM costs
  Benefit cost analysis
Conclusions and lessons learned
Recommendations
Executive summary

## Slide 5: AMS Network
Four arterials in Pasadena:
Maple and Corson access roads plus
Orange Grove and Walnut
Two arterials in Arcadia and Eastward:
(1) Foothill and Duarte via Santa Anita
(2) Colorado and Huntington
Colorado St
Colorado Pl
Duarte Rd
Orange Grove Blvd
Foothill Blvd
Colorado Blvd
Huntington Dr
Corson St
Allen Ave
Hill Ave
Lake Ave
Marengo Ave
Fair Oaks Ave
San Gabriel Blvd
Walnut St
Maple St
Myrtle Ave
Mountain Ave
Buena Vista St
Los Robles
Michililinda Ave
Sierra Madre Villa Ave
Altadena Ave
Santa Anita Ave
Azusa Ave
Freeway network extends
past Azusa toward the east

## Slide 6: Assessment of Corridor Operations
Assess Operations
Select Interventions
Evaluate
Simulate
Create Models
Select Scenarios
Assess Costs
Description of corridor facilities over a larger area
Understanding key transportation challenges
Inventory of field elements

## Slide 7: AADT and Truck Volumes - Freeway
PM 32.89
PM 29.63
PM 26.32
Lake
Avenue
Rosemead
Boulevard
Huntington
Drive
PM 37.86
Irwindale
Avenue
PM 41.59
Grand
Avenue
PM 44.38
PM 39.60
Azusa
Avenue
PM 36.41
PM 24.96
297,000
261,000
266,000
244,000
190,000
136,000
4,390
(2.31%)
11,688
(4.80%)
12,873
(4.84%)
13,534
(5.19%)
9.249
(3.11%)
6,952
(5.11%)
AADT – All Vehicles
AADT – Heavy-Duty Trucks

## Slide 8: Average Freeway Travel Times (Sept 2013)

## Slide 9: Congested Areas
AM Peak
Frequently congested areas
PM Peak

## Slide 10: Major Bottlenecks – AM Peak
Baldwin
Allen
Hill
Lake
Los Robles
Fair Oaks
Altadena
Sierra Madre
Myrtl
Mountain
Buena Vista
Citrus
Grand
San Dimas Canyon
San Dimas Ave
Lone Hill
Amelia
Irwindale
Azusa
Santa Anita
San Gabriel
Heavy entering traffic from consecutive Michillanda, Foothill and Rosemead on-ramps (~1700 vph)
Heavy traffic from Lake on-ramp (~900 vph)
Data source: 2010 Corridor CSMP
Traffic weaving to take Sierra Madre exit
Entering traffic from Mountain and Buena Vista consecutive on-ramps (>600 vph)
Traffic weaving to the outer lanes to take I-605 SB exit
Significant on-ramp traffic (~600 vph)
Heavy entering traffic from two consecutive Baldwin on-ramps
Weaving traffic seeking to take the I-210 NB Connector
Merging traffic from SR-134 and I-210 SB
Heavy entering traffic from consecutive San Gabriel and Altadena on-ramps
(~1400 vph)
Heavy traffic from two consecutive Santa Anita on-ramps (~1000 vph)
Traffic merging at crest of a curve
Heavy traffic from two consecutive on-ramps
(~1000 vph)
Heavy traffic from two consecutive on-ramps
(~1000 vph)
Weaving from mainline traffic trying to get to the outer lanes to take the I-605 exit
Traffic merging at the crest of a large horizontal curve
Traffic merging at the crest of a large horizontal curve
Heavy on-ramp traffic
Traffic entering from consecutive Santa Anita and Huntington on-ramps (~950 vph)
Traffic merging at the crest of a large horizontal curve
Eastbound Bottleneck
Westbound Bottleneck
Frequently Congested Segment

## Slide 11: Major Bottlenecks – PM Peak
Heavy traffic from Lake on-ramp (~800 vph)
Entering traffic from San Gabriel on-ramp (~550 vph)
Baldwin
Allen
Hill
Lake
Los Robles
Fair Oaks
Altadena
Sierra Madre
Myrtl
Mountain
Buena Vista
Citrus
Grand
San Dimas Canyon
San Dimas Ave
Lone Hill
Amelia
Irwindale
Azusa
Santa Anita
San Gabriel
Demand from on-ramps exceeding available mainline capacity
Data source: 2010 Corridor CSMP
Large horizontal curves between San Gabriel and Sierra Madre
Traffic entering from consecutive Rosemead and Michilinda on-ramps with mainline traffic near capacity (~400 vph)
Traffic entering from consecutive Santa Anita and Huntington on-ramps (~1200 vph)
Heavy entering traffic from Mountain and Buena Vista consecutive on-ramps (~1200 vph)
Traffic weaving to take to I-605 SB exit
Heavy traffic from two consecutive on-ramps
(~600 vph)
Heavy traffic from two consecutive on-ramps
(~1200 vph)
Weaving from mainline traffic trying to get to the outer lanes to take the I-605 exit
Heavy traffic from two consecutive Santa Anita on-ramps (~700 vph)
Heavy entering traffic from two consecutive Baldwin on-ramps
Heavy entering traffic from consecutive Michillanda, Foothill and Rosemead on-ramps (~1700 vph)
Weaving from traffic exiting at Sierra Madre
Heavy traffic from Lake on-ramp (~1000 vph)
Weaving from traffic seeking to take the I-210 NB connector
Heavy entering traffic from consecutive San Gabriel and Altadena on-ramps
(~1200 vph)
Merging traffic from SR-134 and I-210 SB
Traffic merging at crest of a curve
Traffic merging at the crest of a large horizontal curve
Traffic merging at the crest of a large horizontal curve
Traffic merging at the crest of a large horizontal curve
Eastbound Bottleneck
Westbound Bottleneck
Frequently Congested Segment

## Slide 12: AM Collisions involving CHP, by Type (2010-2011)

## Slide 13: AM Collisions involving CHP, by Type (2010-2011)

## Slide 14: PM Collisions involving CHP, by Type (2010-2011)

## Slide 15: Freeway – HOV/HOT Lanes
Interchange
Freeway
Arterial
Existing HOV Lane
Existing HOT Lane
HOV Lane in Design Stage
HOV Lane Under Construction
HOV Lane in Planning Stage
Converted to HOT Facility February 2013
Restriction in place 24/7
Entry/Exit Point
Entry Only
Exit Only

## Slide 16: Freeway Ramp Metering Capability
Metered Ramp/Connector
Partially Metered Ramp/Connector
Unmetered Ramp/Connector
HOV Lane
EB
HOV Lane
Mt Olive Ramps
HOV Lane
EB - From SB Azusa
HOV Lane
EB - From SB Citrus
HOV Lanes EB/WB
HOV Lane EB
HOV Lane
WB - From SB Grand
HOV Lane
WB - From SB Foothill
HOV Bypass NB/SB
HOV Bypass NB/SB
HOV Bypass NB
HOV Bypass SB
HOV Bypass SB
HOV Bypass EB
HOV Bypass EB/WB
HOV Bypass WB
HOV Bypass WB
HOV Bypass EB/WB
HOV Bypass
3 of 4 Ramps
HOV Bypass
WB
HOV Bypass
WB
HOV Bypass
WB 1 of 2 Ramps
HOV Bypass
WB 1 of 2 Ramps
HOV Bypass
WB/EB
Vernon Ave
Lake Ave
Baseline Ave
To
2001 SWARM
Test Area
2009
SWARM
Test Area
Currently operating: SATMS - Local Responsive using 170 Controller

## Slide 17: Traffic Signals – TCS Host
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
McCain - QuickNet Pro
SCATS
Siemens - i2tms
Transcore - Series 2000
S
Stop Controlled
Not determined
Transcore - TransSuite
S
S
Transcore - TransSuite (Planned)
S
S
S
S
S
S
S
S
S
S
S
KITS
KITS (Planned)
Inventory as of June 2014

## Slide 18: Detection – Arterial Sensor Types
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
Inductive Loops
None (Stop Sign)
No Detection/ Unknown
Video & Inductive Loops
Video Detection
S
S
S
S
S
S
S
S
S
S
S
S

## Slide 19: Detection – Approach Volume Availability
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S
Pasadena – McCain QuickNet Pro
Pasadena – SCATS
Pasadena – Siemens i2tms
Pasadena – Transcore Series 2000
S
Stop Controlled Intersection
LA County – KITS
Arcadia – Transcore TransSuite
All approches
Some approches
No approach / Not determined
Monrovia – No central system
Duarte – No central system
Coverage
Collection System
S
Caltrans – No central system
S
S
S
S
S
S
S
S
S
S
S
S

## Slide 20: Park & Ride – Facilities
Sierra Madre Villa
Allen
Lake
Del Mar
Fillmore
Mission
Arcadia
Monrovia
Duarte
Irwindale
Alameda
Citrus
Cal State Los Angeles
West Covina
Baldwin Park
El Monte
Metrolink
P 40
P 50
P 130
30
P 102
P 100
P 128
P 2155
P 238
P 231
P 338
P 326
P 300
P 125
P 200
P 200
El Monte Bus Station
P 420
P 94
P 10
P 239
P 88
P 300
P 500
P 55
P 750
P 190
Other Park-and-Ride Lots
P 100
Metro Silver Line
Metro Gold Line
Parking Fee
Gold Line Extension Phase 2A
Caltrans Lots
P 100
Express Bus Lines
Future LA Metro Lots (late 2015)
P 100
Existing LA Metro Lots
Gold Line Extension Phase 2B
$
P 50
P 610
$
P 877
88
Memorial Park
Los Angeles County Lots
P 100
P 100
P 100
P 100
Metrolink Lots
P 366
Paid Reserved Parking
R
R
R
R
Metrolink San Bernardino
P 500
P 70
P 200
P 128
P 655
$
Covina
P 226 .
R
$

## Slide 21: Light-Rail, Transitway and Commuter Rail
Allen
Lake
Memorial Park
Del Mar
Fillmore
Mission
Arcadia
Monrovia
Duarte
Irwindale
Alameda
Citrus
San Dimas (Planned)
El Monte Bus Station
Cal State Los Angeles
West Covina
LA Metro Silver Line
LA Metro Gold Line
Gold Line Foothill Extension Phase 2A
Transit Station
Gold Line Foothil Extension Phase 2B
Metrolink San Bernardino
El Monte Metrolink
Baldwin Park
Covina
Late 2015 Planned Opening
Sierra Madre Villa

## Slide 22: Select Representative Operational Scenarios
Assess Operations
Select Interventions
Evaluate
Simulate
Create Models
Select Scenarios
Assess Costs
Engage stakeholders
Identify problem types we want to fix
Identify scenarios that are representative of corridor operations

## Slide 23: I-210 Pilot Project Goals and Objectives
Initial focus is on managing incidents/events, with gradual expansion to demand management and commute congestion
Develop a pilot system that can be replicated on other corridors and be a model for other corridors in the state and country
Incident/Event
Management
Initial System
Time
Incident/Event
Management
Transit/parking Management
Incident/Event
Management
Transit/parking Management
Commute Traffic Management
Transit Management

## Slide 24: AMS Scenarios
Demand Class | ICM Intervention | No incident | Freeway incident | Arterial incident
High | no |  |  | 
 | yes |  |  | 
Medium | no |  |  | 
 | yes |  |  | 

## Slide 25: Summary of Analysis Settings
Parameter | Comment
Analysis year | 2014 chosen on having available data on the I-210 freeway and some arterials
Time period of analysis | PM peak
Simulation period | 3 PM - 8 PM is the primary analysis period.
Freeway incident location | Chosen to represent an historically accurate and major blockage during the peak period
Freeway incident severity | Major – at least one lane closed
Arterial incident location | Chosen to represent an historically accurate and major blockage during the peak period
Arterial incident severity | Major – at least one lane closed
Incident duration | Chosen to represent an historically accurate and major blockage, for example 30-90 minutes

## Slide 26: Select ICM Intervention Strategies
Assess Operations
Select Interventions
Evaluate
Simulate
Create Models
Select Scenarios
Assess Costs
Engage stakeholders
Identify ICM strategies most appropriate for the challenges at hand
Target infrastructure investments that are realistic

## Slide 27: ICM Strategies
Coordinated freeway-arterial operations
  Coordinated ramp metering and signal synchronization
  Use of arterial capacity to supplement freeway operations
  Use of freeway capacity to supplement arterial operations
Active re-routing around major incidents
  Provide way-finding and actionable travel information in addition to coordinated ramp metering and signal synchronization

## Slide 28: Coordinated arterial-freeway operations
Coordinated ramp metering and signal synchronization
  Provide extra arterial capacity to support increased demand
  Facilitate re-entry onto freeway downstream of incident bottleneck

## Slide 29: Coordinated arterial-freeway operations
Coordinated ramp metering and signal synchronization
  Adjust arterial signals to favor movements around incident location
  Facilitate entry onto freeway upstream of arterial incident location

## Slide 30: Active re-routing around major incidents
Provide way-finding and actionable travel information in addition to coordinated ramp metering and signal synchronization
Accident ahead

## Slide 31: Model Building
Assess Operations
Select Interventions
Evaluate
Simulate
Create Models
Select Scenarios
Assess Costs

## Slide 32: Model Building Process
Data pre-processing
Sanity
Consistency
Engineering judgement
Incomplete information from different years
No-incident
Incident
Incident + intervention
Basic information for model construction
Calibration data
Validation data
Model construction calibration and validation

## Slide 33: Model construction, calibration and validation
Model Construction
Model Calibration
Simulation
Calculation of metrics
Model Validation
Model with calibrated parameters
Density, flow, velocity
Queue length, delay, travel time
Basic model
Calibration Data:
Flows
Travel times
Independent Validation Data:
Flows
Travel times
Basic information:
Network geometry
Speed limits
Signal timing
Rough turning ratios

## Slide 34: Example of arterial data
Coverage of 5-min loop data

## Slide 35: Calibration Guidelines
Calibration Criteria and Measures | Calibration Acceptance Targets
Traffic flows within 15% of observed volumes for links with peak-period volumes greater than 2,000 vph | For 85% of cases for links with peak-period volumes greater than 2,000 vph
 | Separate thresholds for arterials and freeways?
Sum of all link flows | Within 5% of sum of all link counts
Travel times within 15% | For 85% of cases
Recurrent bottleneck congestion | Spatial-temporal match within 30 minutes and 1/2 mile of observed congestion
Incident-related congestion | Duration within 25% of observation
 | Queue propagation within 20% of observation

## Slide 36: Simulate and Assess Performance
Assess Operations
Select Interventions
Evaluate
Simulate
Create Models
Select Scenarios
Assess Costs

## Slide 37: Simulation and Performance Assessment
Flow
Speed
Density
No-incident
Incident
Incident + intervention
Simulation Engine
Performance Measures

## Slide 38: Corridor Performance Measures
Flow
Speed
Density
Travel Time
  during specified time period
  freeway mainline
  freeway  arterial  freeway
Total Delay
Vehicle Hours Traveled
Vehicle Miles Traveled
Person Hours Traveled
Person Miles Traveled
    during specified time period
  by jurisdiction
  by facility
Buffer index for travel time reliability
Emission
  rate (per vehicle)
  total
Fuel Consumption
  rate (per vehicle)
  total
Collision / Fatality
  rate (per million VMT)
  total

## Slide 39: Assess Costs and Evaluate Benefits
Assess Operations
Select Interventions
Evaluate
Simulate
Create Models
Select Scenarios
Assess Costs

## Slide 40: Evaluation of benefits and ICM investments
Infrastructure | Capabilities | Benefits
Existing infrastructure | Ramp metering | Limited benefits
 | Signal synchronization | 
Enhanced infrastructure | Improved ramp metering | Greater benefits
 | Wider-area signal synchronization | 
 | Coordination of ramps and signals | 
 | Active reroutes | 
Calculate costs of enhancements | Evaluate | Calculate benefits of enhancements