## Slide 1: SIMULATION RESULTS

## Slide 2: Why are we modeling traffic?
Simulation of common traffic conditions
  Recurrent congestion
  Incidents
Simulation of potential Response Plans
  Do nothing
  Rerouting
  Adjusted Signal Plans
Evaluation of Response Plans
  VHT

## Slide 3: Outline
What network we are modeling
What we did last time
What we plan to show this time
  Incident modeling
  Response plan

## Slide 4: Outline
What network we are modeling
What we did last time
What we plan to show this time
  Incident modeling
  Response plan

## Slide 5: Network
Colorado St
Colorado Pl
Duarte Rd
Orange Grove Blvd
Foothill Blvd
Colorado Blvd
Huntington Dr
Corson St
Allen Ave
Hill Ave
Lake Ave
Marengo Ave
Fair Oaks Ave
San Gabriel Blvd
Walnut St
Maple St
Myrtle Ave
Mountain Ave
Buena Vista St
Los Robles
Michililinda Ave
Sierra Madre Villa Ave
Altadena Ave
Santa Anita Ave
Azusa Ave
Simulated freeway ~18.5 mi
Simulated arterial ~ 3.3 mi

## Slide 6: Outline
What network we are modeling
What we did last time
What we plan to show this time
  Incident modeling
  Response plan

## Slide 7: Last time we showed
Reproduce typical day
  No-incident
  PM peak period
  Off-peak direction

## Slide 8: The site
19 miles of 210 Westbound from PM 42 to 23.
23 on-ramps, 21 off-ramps.
Heavy morning congestion, light afternoon congestion.
I-605
Huntington St. detour
PM 30
PM 42
PM 23

## Slide 9: Freeway simulation results
I-605
Baldwin
16:20
18:50
Inspection of congestion

## Slide 10: Freeway Observed congestion (PeMS)
bad detection
I-605
Baldwin
16:20
18:50
Inspection of congestion
22-May-2014

## Slide 11: Freeway calibration results
Criterion | 4:00 pm 5:00 pm | 5:00 pm 6:00 pm | 6:00 pm 7:00 pm | 7:00 pm 8:00 pm
flow within 400 vph of measurement | 78% | 78% | 83% | 82%
Individual link GEH < 5 | 78% | 78% | 83% | 67%
Total flow within 5% of measurements |  |  |  | 
Total GEH < 4 |  |  |  | 
~80% of hourly mainline flows are within acceptable limits.
Total flows are within acceptable limits errors balance out.

## Slide 12: I-210 Arterial and Freeway Model
Number of links: 1001
Freeway: 210
Arterial: 791
Number of signalized intersections: 13

## Slide 13: Data - Arterial
On arterial, we only have 5-min loop data at limited locations

## Slide 14: Simulated Westbound traffic on Huntington and Colorado

## Slide 15: Estimated vs. Measured Flows, 16:00-17:00
Individual link flows | Passed cases | Targets
Flow within 100 vph for link flows < 700 vph | 4/5 = 80% | > 85%
Flow within 15% for 700 vph < link flows < 2700 vph | 6/9 = 67% | > 85%
Flow within 400 vph for link flows > 2700 vph | 0/0 | > 85%
GEH statistics < 5 | 10/14 = 71% | > 85%
Sum of all link flows | Results | Targets
Relative Error in Total Flow | 5.4% | < 5%
GEH | 5.5 | < 4

## Slide 16: Outline
What network we are modeling
What we did last time
What we plan to show this time
  Incident modeling
  Response plan

## Slide 17: Definitions
Passive reroute: Drivers exit the freeway and seek an alternate route on the surrounding arterials on their own
Active reroute: System operators use traveler information and wayfinding mechanisms (CMS, trailblazer signs, radio, mobile apps) to actively influence drivers’ route choice

## Slide 18: Today we will show: incident modeling
Reproduce incident day
Additional flow on arterial; caused by passive reroute of drivers

## Slide 19: Today we will show: response plan
Increase cycle length of arterial lights  larger arterial capacity  larger network-wide capacity  less congestion

## Slide 20: Summary of Incident Runs
Run | Story |  |  | VHT
 | Incident | Reroute | Signal Plan | 
1 | No | No | Normal | 9,557 veh*h
2 | Yes | Passive | Normal | 10,245 veh*h
3 | Yes | Passive | Adjusted | 10,173 veh*h (cp. 2: ∆ -72 veh*h)
4 | Yes | Active | Adjusted | 9,919 veh*h (cp. 2: ∆ -326 veh*h)

## Slide 21: Network
Colorado St
Colorado Pl
Duarte Rd
Orange Grove Blvd
Foothill Blvd
Colorado Blvd
Huntington Dr
Corson St
Allen Ave
Hill Ave
Lake Ave
Marengo Ave
Fair Oaks Ave
San Gabriel Blvd
Walnut St
Maple St
Myrtle Ave
Mountain Ave
Buena Vista St
Los Robles
Michililinda Ave
Sierra Madre Villa Ave
Altadena Ave
Santa Anita Ave
Azusa Ave
Simulated freeway ~18.5 mi
Simulated arterial ~ 3.3 mi

## Slide 22: Run 1: No incident “the Baseline”
Freeway,
I210
westbound
Arterial,
Huntington & Colorado westbound
Recurrent
bottleneck
May 22nd, 2014
No incident
No reroute
120s cycle time
Baseline

## Slide 23: Run 1: No incident “the Baseline”
Freeway,
I210
westbound
Arterial,
Huntington & Colorado westbound
Recurrent
bottleneck
May 22nd, 2014
No incident
No reroute
120s cycle time
Baseline

## Slide 24: Run 1: No incident “the Baseline”
Freeway,
I210
westbound
Arterial,
Huntington & Colorado westbound
Recurrent
bottleneck
May 22nd, 2014
No incident
No reroute
120s cycle time
Baseline

## Slide 25: Incident & Reroute
Reroute @exit Huntington from 16:35 to 17:05
Incident on freeway from 16:30 to 17:00;
remaining capacity is 5000 veh/h

## Slide 26: Evidence for Passive Rerouting
+460 veh/hr
during incident
Multiple incidents on I210W downstream of Huntington exit
from 17:30 and 19:00

## Slide 27: Flow @exit Huntington
Off-ramp flow when no incident

## Slide 28: Flow @exit Huntington
Reroute active
16:35-17:05
Rerouted flow
Off-ramp flow when no incident
Increased off-ramp flow during incident due to passive reroute

## Slide 29: Run 2: Incident, 400 veh/h reroute “Passive Reroute, no response plan”
freeway
arterial
Recurrent
bottleneck
Incident duration
Queue extent
Queue ~8mi
Incident
400veh/h reroute
120s cycle time
Based on data

## Slide 30: Run 2: Incident, 400 veh/h reroute “Passive Reroute, no response plan”
freeway
arterial
Recurrent
bottleneck
Incident duration
Queue extent
Queue ~8mi
Incident
400veh/h reroute
120s cycle time
Based on data

## Slide 31: Run 2: Incident, 400 veh/h reroute “Passive Reroute, no response plan”
freeway
arterial
Recurrent
bottleneck
Incident duration
Queue extent
Queue ~8mi
Incident
400veh/h reroute
120s cycle time
Based on data

## Slide 32: Comparison of Contour Plots Run 1: No Incident vs. Run 2: Incident, 400 veh/h reroute
offramp
Significant change in flow on the freeway @offramp Huntington

## Slide 33: Comparison of Contour Plots Run 1: No Incident vs. Run 2: Incident, 400 veh/h reroute
offramp
Significant change in flow on the freeway @exit Huntington
Active Reroute
@exit Huntington

## Slide 34: Comparison of Contour Plots Run 1: No Incident vs. Run 2: Incident, 400 veh/h reroute
offramp
different
same
same
different
same

## Slide 35: Combination with flow @exit Huntington
offramp
different
same
same
different
same

## Slide 36: Run 3: Incident, 400 veh/h reroute, cycle time = 240s “Passive Reroute + Adjusted Signal Plan”
freeway
arterial
Incident duration
Queue extent
Recurrent
bottleneck
Queue ~8mi
Incident
400veh/h reroute
240s cycle time
Passive reroute

## Slide 37: Run 3: Incident, 400 veh/h reroute, cycle time = 240s “Passive Reroute + Adjusted Signal Plan”
freeway
arterial
Incident duration
Queue extent
Recurrent
bottleneck
Queue ~8mi
Incident
400veh/h reroute
240s cycle time
Passive reroute

## Slide 38: Run 3: Incident, 400 veh/h reroute, cycle time = 240s “Passive Reroute + Adjusted Signal Plan”
freeway
arterial
Incident duration
Queue extent
Recurrent
bottleneck
Queue ~8mi
Incident
400veh/h reroute
240s cycle time
Passive reroute

## Slide 39: Flow @exit Huntington
Reroute active
16:35-17:05
Rerouted flow
Off-ramp flow when no incident
Increased off-ramp flow during incident due to passive reroute
Increased off-ramp flow during incident due to active reroute

## Slide 40: Run 4: Incident, 600 veh/h reroute, cycle time = 240s “Active Reroute + Adjusted Signal Plan”
freeway
arterial
Incident duration
Queue extent
Recurrent
bottleneck
Queue ~4mi
Incident
600veh/h reroute
240s cycle time
Active reroute

## Slide 41: Run 4: Incident, 600 veh/h reroute, cycle time = 240s “Active Reroute + Adjusted Signal Plan”
freeway
arterial
Incident duration
Queue extent
Recurrent
bottleneck
Queue ~4mi
Incident
600veh/h reroute
240s cycle time
Active reroute

## Slide 42: Run 4: Incident, 600 veh/h reroute, cycle time = 240s “Active Reroute + Adjusted Signal Plan”
freeway
arterial
Incident duration
Queue extent
Recurrent
bottleneck
Queue ~4mi
Incident
600veh/h reroute
240s cycle time
Active reroute

## Slide 43: Conclusion
Run | Incident y/n | Rerouted flow | Cycle time | Story | VHT | Max length of incident queue
1 | No | 0 veh/h | 120s | No incident, Baseline | 9,557 veh*h | -
2 | Yes | 400 veh/h | 120s | Incident, Passive Reroute | 10,245 veh*h | 8 mi
3 | Yes | 400 veh/h | 240s | Incident, Passive Reroute + Adjusted Signal Plan | 10,173 veh*h (cp. 2: ∆ -72 veh*h) | 8 mi
4 | Yes | 600 veh/h | 240s | Incident, Active Reroute + Adjusted Signal Plan | 9,919 veh*h (cp. 2: ∆ -326 veh*h) | 4 mi
We have a tool to
Simulate different traffic conditions
Simulate Response Plans
Evaluate Response Plans